## Slide 1: G4Beamline A “Swiss Army Knife” for Geant4 http://g4beamline.muonsinc.com
Tom Roberts
Muons, Inc.

## Slide 2: Basic Approach
Implement a general, flexible, and extensible program for Geant4 simulations, optimized for beamlines.
In practice, it is much more general than just beamlines (e.g. there is a cosmic-ray “beam”)
Requires no programming by users, but is sophisticated enough to simulate the Study II SFoFo Cooling Channel, and flexible enough to do the MICE beamline and cosmic-ray studies.
Use a straightforward ASCII input file to completely determine the simulation.
Provide user-friendly input generation, visualization of the system, and analysis of the simulation results.
Include realistic and accurate particle tracking and interactions (incl. EM, weak, and hadronic).
Include support for scripting and parallel jobs on a cluster

## Slide 3: Using the Program
The basic idea is to define each beamline element, and then place each one into the beamline at the appropriate place(s).
All aspects of the simulation are specified in a single ASCII input file:
  Geometry
  Input Beam
  Physics processes
  Program control parameters
  Generation of output NTuples
The input file consists of a sequence of commands with named arguments
Each command has its own list of arguments
Command and argument names are spelled out, so the input file becomes a record of the simulation that is readable by others

## Slide 4: Using the Program
The beamline elements implemented are:
  absorber – a material absorber with shaped containment and safety windows
  box – a material in the shape of a box
  corner – rotate the centerline coordinates, for bend or secondary target
  cosmicraybeam – a “beam” of cosmic-ray muons
  fieldmap – read a field map from a file, for E and/or B
  genericbend – a generic bending magnet
  genericquad – a generic quadrupole magnet
  helicaldipole – a helical dipole magnet for 6-D muon cooling
  idealsectorbend – a sector bending magnet
  pillbox – a pillbox RF cavity, including optional windows
  polycone – a material in the shape of multiple cones
  solenoid – a single-coil magnet
  sphere – a material in the shape of a sphere
  trap – a material in the shape of a trapezoid
  tubs – a material in the shape of a cylinder or pipe
  virtualdetector – a ‘perfect’ detector for monitoring the beam

## Slide 5: Using the Program
Simulation control commands:
  beam – specify the incoming beam (from a file or randomly generated)
  reference – specify a reference particle
  place – position a previously-defined object into the simulation
  material – specify the properties of a new material
  geometry – perform geometrical tests for invalid intersections of objects
  param – define parameters for program or input file
  particlecolor – specify the display colors for particle types
  particlefilter – cut particles by type or momentum, force decays, etc.
  physics – defines the physics processes and controls them
  trackcuts – impose specific cuts on tracks
Beamline layout commands:
  start – defines the starting point and orientation of the beamline
  corner – inserts a corner into the Centerline coordinates
  cornerarc – inserts a corner into the Centerline coordinates, with path length of an arc

## Slide 6: Using the Program
Complex manual procedures have been automated:
  Field maps of solenoids can be automatically determined by specifying the required accuracy
  RF Cavities can be tuned, for timing and gradient; both can be fixed or automatically tuned
Geometry layout has been vastly simplified
  Beam elements are simply lined up along the Z axis
  Centerline coordinates behave naturally for bending magnets or secondary targets
  Elements may overlap (e.g. nested pipes), but not intersect
  Many elements can be the parent of other elements
  Specific offsets in X, Y, and/or Z can be specified when needed
  Rotations are specified naturally
    Y30,Z90 is a 30 degree rotation around Y followed by a 90 degree rotation around Z
    Axes are for the parent volume and thus do not change
  Automatic geometry testing detects invalid intersections
All of the Geant4 8.1 physics use cases are available by name.
Beam tracks can be generated internally, or read from a file
Most Geant4 visualization drivers are supported by name.
  Open Inventor is included, and is by far the most user friendly

## Slide 7: Using the Program
The result is a program that reduces the complexity of the user input to that of the system being simulated (a major drawback of any simulation program, including those using Geant4, is that C++ simulation code is considerably more complex than the problem).
While C++ programming is not required to use the program, knowledge of the problem domain is absolutely required, as is enough experience to distinguish sensible results from nonsense.
Visualization is highly recommended, to verify that the geometry is correct and makes sense.

## Slide 8: Example Uses – MICE

## Slide 9: Example Uses – 6D Muon Cooling

## Slide 10: Example Uses – Cosmic Ray Tomography

## Slide 11: example1.in
# example1.in – put beam into 4 detectors
physics LHEP_BIC
beam gaussian particle=mu+ nEvents=1000 beamZ=0.0 \
sigmaX=10.0 sigmaY=10.0 sigmaXp=0.100 sigmaYp=0.100 \
meanMomentum=200.0 sigmaP=4.0 meanT=0.0 sigmaT=0.0
# BeamVis just shows where the beam comes from
Box BeamVis width=100.0 height=100.0 length=0.1 color=1,0,0
# define the detector (used 4 times)
detector Det radius=1000.0 color=0,1,0
# place BeamVis and four detectors, putting their number into their names
place BeamVis z=0
place Det z=1000.0 rename=Det#
place Det z=2000.0 rename=Det#
place Det z=3000.0 rename=Det#
place Det z=4000.0 rename=Det#

## Slide 12
example1.in
Visualizations of example1.in,
using OpenGL (above), and
OpenInventor (right). Above is
a plan view, while at right is a
3-D view.

## Slide 13
example2.in (4 cells from Study 2)

## Slide 14: Demonstration of interactive capabilities
Visualization of the MICE beamline via Open Inventor
Generation of histograms and manipulating them via HistoRoot

## Slide 15: Summary
G4Beamline is a simulation program capable of accurate and realistic simulation via single-particle tracking.
It has an intuitive, user-friendly interface that reflects the complexity of the problem, and is directly readable by physicists familiar with the problem domain.
Simulations of complex accelerator structures can be performed without C++ programming.
http://g4beamline.muonsinc.com